Build Your First Kernel Patch
and
Submit It
AceLan Kao
2013/08/04

---
http://people.canonical.com/~acelan/coscup-2013/

---
Introduction
- What can we fix (in the beginning)
- Key/ACPI/WMI events
- monitor WMI event by ftrace
- BIOS & OSI
- rfkill
- branch and add your code
- build patch and check it
- submit

---
What can we fix
- brightness/volume function key doesn't work, or adjust twice by one key stroke
- display toggle key
- wifi/bt can't enable/disable by function key
- wifi/bt LED doesn't sync with its status
NOTE. You need the latest source code
MAINTAINERS in kernel source
drivers/platform/x86

---
Key/ACPI/WMI event
- Keyevent
    - could be observed by showkey command
    - /proc/bus/input/devices & /lib/udev/keymap
    - EC, ACPI, WMI
- ACPI event
    - acpi_listen
    - /sys/module/video/parameters/brightness_switch_enabled
    - drivers/acpi/video.c

---
Monitor WMI event by ftrace
- check which wmi driver do you use
    - lsmod | grep wmi
- /sys/kernel/debug/tracing
- echo :mod:dell_wmi > set_ftrace_filter
- echo function > current_tracer
- cat trace
- echo nop > current_tracer
- http://people.canonical.com/~acelan/2010-aka-linux/

---
BIOS & _OSI
- March 2009: Removed "Linux"
- We are MS Windows
    - Win7 before kernel v3.7
    - Win8 since kernel v3.7-rc1
- NOTE. drivers/acpi/acpica/utosi.c
    - acpi_osi="!Windows 2012"

---
rfkill
- rfkill list
    - H/W device and virtual device
    - hard block and soft block
- rfkill block/unblock
- /sys/class/rfkill
27e49ca rfkill: Add the capability to switch all devices of all type in __rfkill_switch_all().

---
branch and add your code
- build your driver apart from the whole kernel
    - copy the driver directory to somewhere
    - mv Makefile Kbuild
    - copy Makefile from my directory
    - modify Kbuild
    - make
ifeq (,$(KVER))
        KERNELBUILD := /lib/modules/`uname -r`/build
else
        KERNELBUILD := /lib/modules/$(KVER)/build
endif
all:
        make -C $(KERNELBUILD) M=$(shell pwd) modules
clean:
        make -C $(KERNELBUILD) M=$(shell pwd) clean

---
branch and add your code(cont.)
- DKMS
    - dkms.conf
PACKAGE_NAME="video"
PACKAGE_VERSION="1.0"
AUTOINSTALL="yes"
MAKE="make KVER=$kernelver"
CLEAN="make KVER=$kernelver clean"
BUILT_MODULE_NAME[0]="video"
BUILT_MODULE_LOCATION[0]="./"
DEST_MODULE_LOCATION[0]="/updates/kernel/"

---
branch and add your code(cont.)
- DKMS
    - cp -a video-1.0 /usr/src
    - sudo dkms add -m video -v 1.0
    - sudo dkms build -m video -v 1.0
    - (sudo dkms install -m video -v 1.0)
    - sudo dkms mkdeb -m video -v 1.0
    - (sudo dkms remove -m video -v 1.0)
    - /var/lib/dkms/video/1.0

---
branch and add your code(cont.)
- git checkout -b new_branch
- apply your fix & git commit -a -e -s
- commit log should contain
    - what have you fixed
    - the problem user may encounter without the fix
    - Error message if any
- ex. 16a3d9f thinkpad-acpi: enable loading module with new B-series Lenovo BIOS

---
Submit your patch
- check the coding style of the patch
    - scripts/checkpatch.pl
- setup msmtp
- check MAINTAINERS or ./scripts/get_maintainer.pl
ASUS NOTEBOOKS AND EEEPC ACPI/WMI EXTRAS DRIVERS
M: Corentin Chary <corentin.chary@gmail.com>
L: acpi4asus-user@lists.sourceforge.net
L: platform-driver-x86@vger.kernel.org
W: http://acpi4asus.sf.net
S: Maintained
F: drivers/platform/x86/asus*.c
F: drivers/platform/x86/eeepc*.c

---
Submit your patch(cont.)
git send-email --no-chain-reply-to --thread --suppress-cc all --smtp-server /usr/bin/msmtp --from 'AceLan Kao <acelan.kao@canonical.com>' --to "linux-bluetooth@vger.kernel.org" --to "Marcel Holtmann <marcel@holtmann.org>" --to "Gustavo Padovan <gustavo@padovan.org>" --to "Johan Hedberg <johan.hedberg@gmail.com>" 0001-Bluetooth-Add-support-for-Atheros-0cf3-3121.patch

---
Reference
- git://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux-2.6.git
- git log drivers/platform/x86
- Documentation/trace/ftrace.txt
- LKML(Linux Kernel Mailing List)
- https://bugs.launchpad.net/ubuntu/+source/linux