Linux Kernel Debugging
A Hardware Enabling Introduction
Presentation by
Eric Miao
eric.miao@canonical.com
www.canonical.com
Dec 2011

---
Agenda
- Kernel debug – general introduction
- Debug Boot
- Debug Hotkeys
- Debug Backlight
- Debug Suspend/Resume

---
Kernel Debug – General Introduction
  - printk()
    - change the ring buffer size
    - change the debug levels (/proc/sys/kernel/pringk)
  - Serial console
    - RS232 on the back (console=ttyS0,115200n8)
    - USB serial
  - GDB
    - gdb on vmlinux
    - kgdb
  - sysrq
  - Objdump for disassembly (useful for kernel oops)
  - kdump

---
Debug Hotkeys - Architecture
scancode is hardware specific
keycode is fully defined, e.g. KEY_VOLUMEUP
driver will translate scancode to keycode
driver will translate WMI/ACPI events to keycode
translation driven by map
map configured by udev

---
Debug Hotkey - Howto
  - Make sure required drivers are there
    - input-utils
  - Make sure driver captured raw events
    - printk() or ftrace in kernel driver
  - Make sure correct keycode reported
    - xev, evtest, input-utils
  - Check the udev keymap table
    - /lib/udev/rules.d/95-keymap.rules
    - /lib/udev/keymaps/*

---
Debug Backlight - Architecture
gnome-setting-daemon
notify-osd
xbacklight
polkit helper
XRandR
gsd-backlight-herlper
X Server
input
Graphics Driver
/sys/class/backlight
    - Brightness events are issued by input drivers (see Debug Hotkeys)
    - gnome-setting-daemon controls logic
    - Brightness control normally done with sysfs node
    - OSD events processed by notify-osd

---
Debug Backlight - Howto
  - Check brightness key events
    - KEY_BRIGHTNESSUP, KEY_BRIGHTNESSDOWN
  - Check brightness control
    - /sys/class/backlight/*/brightness
    - a simple test “echo [brightness] > /sys/class/backlight/*/brightness”
  - Check the user space (in case of using Gnome)
    - gnome-setting-daemon is started OK
    - notify-osd is running
    - dbus-daemon is running

---
Debug Boot - Flow
  1. BIOS initializes hardware and load boot code from booting storage
  2. GRUB loads itself from disk and takes control
  3. GRUB loads the kernel and initramfs according to configuration or user's input
  4. Kernel boots up and hands over the control to init on initramfs
  5. initramfs searches for the correct boot device
  6. initramfs passes control to the init on the boot device
  7. init on the boot device takes control (upstart in case of Ubuntu), and starts the required services/daemons for booting up
  8. GDM or LightDM started by upstart in the final stage
  9. Other desktop related services started by the GUI session manager

---
Debug Boot - Howto
  - Boot options
    - SHIFT key to interrupt GRUB boot
    - 'debug' on kernel command line, remove 'quiet' and 'splash' to allow more kernel messages to output
    - kernel-parameters.txt for reference of kernel command line options
  - Initramfs
    - with 'debug' on kernel command line, log will be in /tmp/initramfs.debug
    - 'break' or 'break=[option]' on kernel command line will break initramfs boot at different stage
  - Upstart
    - Ubuntu is using upstart as init daemon
    - config files in /etc/init/
    - rsyslogd takes control of kernel logging (started very early)
    - /etc/rsyslog.conf and /etc/rsyslog.d/*

---
Debug Suspend/Resume - Overview
  1. echo 'mem' > /sys/power/state will trigger suspend to RAM
  2. freeze of the processes
  3. suspend of devices, CPUs
  4. platform specific suspend (e.g. calling into ACPI)
  5. wake up event occurs
  6. platform specific resume (e.g. BIOS)
  7. passes control to kernel
  8. resume of CPUs and devices
  9. thaw of the frozen processes
  10. resumes execution

---
Debug Suspend/Resume - Howto
    - Do a suspend/resume and check kernel message (dmesg or /var/log/syslog)
    - Boot with 'no_console_suspend' in kernel command line
      - no messages will be logged as rsyslogd has been frozen
      - console will be suspended so no debug messages until it resumed
    - pm_trace
      - enable pm_trace by 'echo 1 > /sys/power/pm_trace'
      - will give more tracing messages
    - Rule out the problem at different stages with pm_test
      cat /sys/power/pm_test
      [none] core processors platform devices freezer
    - When things go tough
      - serial console through UART or ethernet console
      - low level debugging code inserted to critical points (e.g. keyboard LED blinking)

---
Questions please
Thank you
Reference could be found at:
https://wiki.ubuntu.com/Kernel/Debugging